## Slide 1: Issues and Explanation
The EOPs for all the images, when compared to output of BASC and Lab 2, the difference is of the order of
The principal distance, c, when compared to output of BASC and Lab 2, the difference is of the order of
The difference between the values can be attributed to the assumption that object plane is flat
The residuals are of the order of
The RMSE when compared to Lab 2’s square root of variance are very close
For image 10 and 18, the c was imaginary. It would occur in instances when images are very vertical.
To address this issue, c was manually set to 8.16
The major issue for this lab was with debugging the code
While coding the mathematical equations, a misplaced plus or minus within the code let to wrong output
Debugging required a lot of focus because of the number of equations and variables in the model

## Slide 2: Computer Pseudo Code
main.m
  Declare common parameters -> IOPs, Ground co-ordinates of targets
  For each image:
    Get image co-ordinates for each image
    Call LSA.m function
LSA.m
Remove distortions from image co-ordinates remove_dist.m
Calculate A matrix by calling calc_A.m
Calculate y matrix by calling calc_y.m
Calculate x_hat by calling calc_x_hat.m
Calculate c, X0, Y0, Z0
Calculate S matrix by calling calc_S.m
Calculate omega phi kappa by calling calc_opk.m
Calculate residuals by calling residuals.m
Code on Github:
https://github.com/Salazar-Prime/photogrammetry/tree/master/Project%203

## Slide 3: Computer Pseudo Code
Calc_A.m
  Calculate A for both X and Y
Calc_y.m
Calculate y by alternating xi and yi without distortions
Calc_S.m
Loop over all GCPs
get xi quaternion and normalize it
get Xi quaternion and normalize it
multiply C for both quaternions to get Si
sum Si to get the S matrix
Code on Github:
https://github.com/Salazar-Prime/photogrammetry/tree/master/Project%203
remove_dist.m
  Calculate radial distortion
  Calculate de-centering lens distortion
  Subtract from image co-ordiantes
Calc_x_hat.m
x_hat = inv(A'*A)*A'*y;

## Slide 4: Computer Pseudo Code
Code on Github:
https://github.com/Salazar-Prime/photogrammetry/tree/master/Project%203
Calc_opk.m
  Get eigenvalue and eigenvector for S
  Get the eigen vector against maximum eigenvalue
  Get rotation matrix
  Calculate Omega, Phi, kappa from rotation matrix

## Slide 5: Compute Code – main.m
%% Common Parameters
% IOPs
IOP = [6.7451660984e-2,-1.1709829919e-1,8.1671200690];
dist = [-2.9350008918e-4, 9.2190322166e-6,-2.2562559450e-7,6.1878890685e-5,-7.2907688047e-5,0];
% Ground co-ordinates of targets
XA = [-0.044038221723;0.89829592555;1.8428648416;2.7928032424;3.731135328;-0.036927916146;0.90108606018;1.8511589932;2.8010339963;3.7422959221;-0.037704361429;0.90892725171;1.8588605461;2.8062554595;3.7520655984;-0.024722332105;0.91454137562;1.8596674595;2.8078118825;3.7544680979;0;0.9263914178;1.8642980884;2.8111736654;3.7628755375];
YA = [3.751130948;3.7594793917;3.7736433303;3.7823238561;3.7801397656;2.8057675589;2.8180218203;2.8257925207;2.8332144474;2.8378518827;1.8634346772;1.8678901457;1.8758730363;1.8838128654;1.8922797004;0.91840024749;0.92066047041;0.92760553219;0.93553829291;0.94557055946;0;-0.00026178267339;-0.0021390199929;-0.0019752230297;0];
ZA = [0.072640804133;0.048121990404;0;-0.047649472361;-0.070838477818;0.054102199693;0.026008316122;0.0059282538012;-0.023295585379;-0.044574905144;0.016369939657;0.010208246675;0.0071618170061;-0.0096698096332;-0.020910207448;-0.0091692255168;0.003877584251;0.003049069041;-0.0030509411619;-0.0098127723745;0;0.017342094476;0.016047411487;0.006582607018;0];
%% Image 1 - image_09
[EOP_basc,xa,ya] = data(9); % get data for image 9
[c,EOP,res_x,res_y] = LSA(xa,ya,XA,YA,ZA,IOP,dist)
%% Image 1 - image_10
[EOP_basc,xa,ya] = data(10); % get data for image 10
[c,EOP,res_x,res_y] = LSA(xa,ya,XA(1:24),YA(1:24),ZA(1:24),IOP,dist)
%% Image 1 - image_14
[EOP_basc,xa,ya] = data(14); % get data for image 14
[c,EOP,res_x,res_y] = LSA(xa,ya,XA([3:5,7:10,12:15,17:20,22:25]),YA([3:5,7:10,12:15,17:20,22:25]),ZA([3:5,7:10,12:15,17:20,22:25]),IOP,dist);
%% Image 1 - image_18
[EOP_basc,xa,ya] = data(18); % get data for image 18
[c,EOP,res_x,res_y] = LSA(xa,ya,XA,YA,ZA,IOP,dist)
Code on Github:
https://github.com/Salazar-Prime/photogrammetry/tree/master/Project%203

## Slide 6: Compute Code – LSA.m
function [c,EOP,res_x,res_y] = LSA(xa,ya,XA,YA,ZA,IOP,dist)
%% parameters
num_GCP = length(xa);
% Unpack IOPs
[xp,yp,~] = assign_IOP(IOP);
%% A and y matrix
[xa,ya] = remove_dist(xa,ya,dist,xp,yp);
[A] = calc_A(num_GCP,xa,ya,XA,YA);
[y] = calc_y(xa,ya);
%% calculate x_hat
[C1,C2,C3,C4,C5,C6,C7,C8] = calc_x_hat(A,y);
%% calculate c
c = sqrt(-1 * (C1*C2+C4*C5)/(C7*C8));
if not(isreal(c))
c = 8.1671200690;
end
%% calculate A'*A
A = [C1,C4,C7;C2,C5,C8;C3,C6,1]*[1,0,0;0,1,0;0,0,c*c]*[C1,C2,C3;C4,C5,C6;C7,C8,1];
%% calculate EOP (X0,Y0,Z0)
X0 = - A(1,3)/A(1,1);
Y0 = - A(2,3)/A(1,1);
Z0 = sqrt(A(3,3)/A(1,1) - X0^2 - Y0^2);
%% calculate EOP (omega,phi,kappa)
S = calc_S(num_GCP,xa,ya,xp,yp,c,XA,YA,ZA,X0,Y0,Z0);
[omega,phi,kappa] = calc_opk(S);
EOP = [X0,Y0,Z0,rad2deg(omega),rad2deg(phi),rad2deg(kappa)];
%% residuals
[res_x,res_y] = residuals(C1,C2,C3,C4,C5,C6,C7,C8,xa,ya,XA,YA);
end
Code on Github:
https://github.com/Salazar-Prime/photogrammetry/tree/master/Project%203

## Slide 7: Compute Code – calc_A.m
function [A] = calc_A(num_GCP,xa,ya,XA,YA)
% create an empty A matrix
A = zeros(num_GCP*2,8);
% loop over all ground control points
for i=1:num_GCP
A(2*i-1,:) = [XA(i),YA(i),1, 0,0,0, -1*xa(i)*XA(i), -1*xa(i)*YA(i)];
A(2*i, :) = [0,0,0, XA(i),YA(i),1, -1*ya(i)*XA(i), -1*ya(i)*YA(i)];
end
Compute Code – calc_y.m
function [y] = calc_y(xa,ya)
% alternate merge in order : xa, ya
y = [xa ya]';
y = y(:);
end
Code on Github:
https://github.com/Salazar-Prime/photogrammetry/tree/master/Project%203

## Slide 8: Compute Code – calc_x_hat.m
function [C1,C2,C3,C4,C5,C6,C7,C8] = calc_x_hat(A,y)
x_hat = inv(A'*A)*A'*y;
C1 = x_hat(1);
C2 = x_hat(2);
C3 = x_hat(3);
C4 = x_hat(4);
C5 = x_hat(5);
C6 = x_hat(6);
C7 = x_hat(7);
C8 = x_hat(8);
end
Compute Code – calc_S.m
function [S] = calc_S(num_GCP,xa,ya,xp,yp,c,XA,YA,ZA,X0,Y0,Z0)
S = zeros(4,4);
for i=1:num_GCP
xi = [0,xa(i),ya(i),-c];
xi = xi/norm(xi);
Xi = [0,XA(i)-X0,YA(i)-Y0,ZA(i)-Z0];
Xi = Xi/norm(Xi);
mat1 = [xi(1),-xi(2),-xi(3),-xi(4);
xi(2), xi(1), xi(4),-xi(3);
xi(3),-xi(4), xi(1), xi(2);
xi(4), xi(3),-xi(2), xi(1)];
mat2 = [Xi(1),-Xi(2),-Xi(3),-Xi(4);
Xi(2), Xi(1),-Xi(4), Xi(3);
Xi(3), Xi(4), Xi(1),-Xi(2);
Xi(4),-Xi(3), Xi(2), Xi(1)];
S = S + mat1'*mat2;
trace(mat1*mat2)
end
end

## Slide 9: Compute Code – residuals.m
function [res_x,res_y] = residuals(C1,C2,C3,C4,C5,C6,C7,C8,xa,ya,XA,YA)
res_x = xa - (C1*XA + C2*YA + C3)./(C7*XA+C8*YA+1);
res_y = ya - (C4*XA + C5*YA + C6)./(C7*XA+C8*YA+1);
end
Compute Code – calc_opk.m
function [omega,phi,kappa] = calc_opk(S)
[V,D] = eig(S);
[~,id] = sort(diag(D),'descend');
ev = V(:,id(1));
% quat2rotm(ev')
r13 = 2*ev(2)*ev(4) + 2*ev(1)*ev(3);
r12 = 2*ev(2)*ev(3) - 2*ev(1)*ev(4);
r11 = ev(2)^2 + ev(1)^2 - ev(3)^2 - ev(4)^2;
r23 = 2*ev(3)*ev(4) - 2*ev(1)*ev(2);
r33 = ev(4)^2 + ev(1)^2 - ev(3)^2 - ev(2)^2;
phi = asin(r13); % r13
kappa = atan2(-r12/cos(phi),r11/cos(phi))
omega = atan2(-r23/cos(phi),r33/cos(phi))
end
Code on Github:
https://github.com/Salazar-Prime/photogrammetry/tree/master/Project%203

## Slide 10: Compute Code – data.py
function [EOP_basc,xa,ya]=data(image_no)
switch image_no
case 9
EOP_basc = [1.88968674,3.03586621,3.73500036,-19.1841784,-4.34497759,2.05014903];
xa = [-5.3877;-2.92187;-0.49439;1.79834;3.93369;-5.04787;-2.77407;-0.55643;1.5572;3.55246;-4.71235;-2.63868;-0.61275;1.34004;3.19895;-4.43154;-2.5313;-0.66436;1.1514;2.88537;-4.19557;-2.4407;-0.70131;0.99217;2.62277];
ya = [4.93742;4.84433;4.68172;4.49867;4.29866;2.42494;2.3434;2.23887;2.1432;2.04441;0.30738;0.24322;0.17794;0.13305;0.09228;-1.49013;-1.53833;-1.5756;-1.59753;-1.59671;-3.02777;-3.06606;-3.09871;-3.09563;-3.07743];
case 10
EOP_basc = [1.68045678e+000 2.16587520e+000 3.50855335e+000 -4.14855263e-001 -4.93725230e+000 9.24769326e+001];
xa = [4.2568;4.0854;3.8851;3.68;3.479;1.9221;1.7977;1.6796;1.555;1.4339;-0.3967;-0.4724;-0.5334;-0.5915;-0.6454;-2.6632;-2.71;-2.7285;-2.7338;-2.7224;-4.81;-4.8779;-4.8782;-4.8346];
ya= [4.6788;2.3093;0.0418;-2.0823;-4.0521;4.7589;2.3888;0.1175;-2.0216;-4.02;4.8045;2.45;0.1921;-1.9492;-3.9707;4.8258;2.5321;0.2918;-1.8528;-3.8693;4.8076;2.5851;0.3697;-1.7626];
case 14
EOP_basc = [1.00952899e+000 2.53318361e+000 2.80635782e+000 -8.94008150e+000 -1.70515538e+001 9.11810993e+001];
xa = [5.0408;4.5063;4.0613;2.4057;2.1457;1.9236;1.7394;-0.5466;-0.5072;-0.48;-0.4562;-3.1775;-2.9114;-2.6867;-2.495;-5.4743;-5.0707;-4.6992;-4.374];
ya = [-0.3354;-2.7179;-4.6482;2.6935;-0.1767;-2.5023;-4.414;2.7038;-0.0294;-2.2763;-4.1595;2.7274;0.1323;-2.0413;-3.8797;2.7125;0.2538;-1.841;-3.6312];
case 18
EOP_basc = [2.10162316e+000 1.19465520e+000 3.69958966e+000 1.33667830e+001 1.46559054e+000 9.02308070e+001];
xa = [3.2893;3.295;3.2772;3.2471;3.2149;1.5691;1.574;1.5795;1.5697;1.557;-0.3378;-0.3441;-0.3375;-0.3381;-0.3412;-2.4459;-2.481;-2.4964;-2.5036;-2.4987;-4.7066;-4.8269;-4.8928;-4.9179;-4.8917];
ya = [3.8357;2.0059;0.1629;-1.6697;-3.476;4.0453;2.1277;0.1844;-1.7649;-3.6961;4.2673;2.2563;0.2058;-1.8635;-3.9356;4.4805;2.4023;0.2466;-1.9536;-4.1554;4.6783;2.5441;0.2765;-2.0524;-4.369];
end
end

## Slide 11
Compute Code – assign_IOP.py
function [xp,yp,c]=assign_IOP(IOP)
xp = IOP(1);
yp = IOP(2);
c = IOP(3);
end
Code on Github:
https://github.com/Salazar-Prime/photogrammetry/tree/master/Project%203